Title: Observation and Verification of nMOS characteristics.
1. Objectives:
1. To find the MOS model parameters for the transisotrs and then by “pencil & paper” manually calculate the DC characteristics of IDS current vs VDS voltage, using simple current equations for MOS model Level 1 to determine a number of corresponding value pairs of (IDS ; VDS) with gate-source voltage , VGS = a constant > Vth.
2. Use circuit simulator of Micro-wind to do a DC simulation of the IDS current vs VDS voltage and the result of the two methods compared
3. Calculation of the threshold voltage.
1. Aparatus:
  1. Microwind software.
2. Theory: The nMOS transistor IDS current versus VDS voltage equations are as follows:
  1. Cut-off mode: IDS = 0 when VGS < 0.
  2. Triod/Linear region: IDS = k_n lbrace (V_GS -V_Th)V_DS - 1 over 2V_DS^2 rbrace when VDS < VGS – Vth ----(1)
    In Level 1 SPICE model, IDS = %mu_0.{%epsilon_0 %epsilon_{SiO_2}} over T_ox. W over L lbrace ( V_GS-V_Th)V_DS-1over2V_DS^2 rbrace
  3. Saturation egion: IDS = 1 over 2 k_n lbrace (V_GS-V_Th)^2 (1+%lambda V_DS) rbrace when VDS >VGS-Vth --------(2)
    In level 1 SPICE model IDS = %mu_0.{%epsilon_0 %epsilon_{SiO_2}} over T_ox. W over L ( V_GS-V_Th)^2
    when channel modulation effect is neglected the drain current equation (2) can be simplified as IDS = 1 over 2 k_n lbrace (V_GS - V_Th)^2 rbrace when VDS > VGS – Vth -------------------------------------------(3)
The current gain factor kn is a constant with unit . This is dependent on MOS transistor geometry (channel length L and channel width W), fabrication process parameters (electron mobility, µn and gate-oxide capacitance COX ).
The factor kn can be calculated as kn = k '_n W over L where the process conductance parameter k'_n = %mu_n C_ox [ A over V^2 ] . The parameters COX stands for gate oxide capacitance per unit area dependent on gate oxide thickness tOX. This can be expressed as C_OX = %epsilon_ox over t_ox where the %epsilon_ox= 3.97 is the silicone dioxide permitivity which can be calculated with the knowledge of relative dielectric constant value of silicon dioxide %epsilon_{SiO_2} and dielectric constant of vacuuam %epsilon_0 . So %epsilon_ox = %epsilon_{ SiO_2 }* %epsilon_0 . The additional parameter of the IDS and VDS is the threshold voltage VT . The threshold voltage with zero source-substrate (bulk) voltage can be expressed as VT0 . When the source-substrate (bulk) voltage VSB is not equal to zero then we call it for nMOS transistor is Vtn and for pMOS is Vtp can be expressed as follows:
V_{T_n} = V_{{T_0}_n} + %gamma( sqrt{2%phi_b+ abs V_SB} - sqrt{2%phi_b})
V_{T_p} = V_{{T_0}_p} + %gamma( sqrt{2%phi_b+ (V_DD + abs V_BS ) } - sqrt{2%phi_b})
The table below shows the SPICE MOSFET parameters in level 1
Microwind SPICE symbol	Meaning	Theoritical Symbol	Unit
VTO	Threshold Voltage	VT0	V
TOX	Oxide thickness	tox	nm
UO	Low-field obility	%mu_0	m^2 over{ V.sec}
PHI	Surface potential	2 abs %phi	V
GAMMA	Body-bias coefficient	%gamma	V2

1. Procedure:
  1. Level 1 MOS model equations to calculate DC values for the drain current IDS vs drain-source voltage VDS.
    - First calculate with a gate-source voltage VGS = +2.0 V, for each drain-source voltage VDS; 0.5, 1.0, 1.5, 2.0, 2.5 the difference VDS - ( VGS – Vtn) to determine in which region transistor work.. Mark in table 2 equation umber 1 or 2 that should be chosen to calculate the drain current IDS for the correspondingpoint (IDS,VDS) . If we consider the 0.25um CMOS processing technology then Vth = 0.45V, %mu_0=%mu_n=0.06, %gamma=0.4, t_ox =0.5nm
    - Calculate for the voltages VDS: 0.5, 1.0, 1.5, 2.0, 2.5 volts the drain-current IDS for each point (IDS;VDS) after having determined a region the transistor works in (linear or saturated) Fill in corresponding value pairs (IDS;VDS) in table 2 for given drain-source DC voltages.
VDS	0.5	1.0	1.5	2.0	2.5
VDS-(VGS-Vtn)	eqn-1	eqn-1	eqn-1	eqn-2	eqn-2
Manual Calculation IDS (uA)	547.56	884.52	1010.88	1011.933	1011.93

    - Now plot the characteristics curve using excel based data-values of table 1 the curve is like as shown in figure

      Fig 1: Characteristics of nMOS transistor
      Vds (V) -->
      Ids (uA)

Use of “Simulate>MOS characteristics” to generate the DC characteristic IDSn vs VDSn for the nMOS transistor in microwind.
- Open the microwind window and check that the selected foundary is 0.25 um CMOS process from file→ select foundary and choose cmos025.rul. Use Level 1 MOS transistor model.
- Now generate the nMOS transistor of width and length ratio is 4 %lambda x 2%lambda from palate. Then simulate the generated nMOS to check its characteristics curve and compare the curve with the manually generated curve.

Fig 2: Microwind generated nMOS characteristics curve

Conclusion: The characteristics curve of nMOS from manually calculated values of IDS doesn’t vary significantly from automatically generated characteristics curve using Micro-wind. Micro-wind being a simulation software can include several influencing factor while plotting the characteristics curve.